## Slide 1: IDENTIFYING AUTOMATED DRIVING SYSTEMS - DEDICATED VEHICLES (ADS-DV) PASSENGER ISSUES FOR PERSONS WITH DISABILITIES (SAE J3171 )
  Rebecca A. Grier, Ph.D.
  Ford AV LLC
Presentation is an overview of SAE J3171 –an information report written by a volunteer task force. This is not work done by Ford Motor Company or Ford AV LLC.

## Slide 2: Limited Scope
Only vehicle design issues unique to Level 4 & 5 ADS-DVs (i.e., no steering wheel/ pedals for human driver)
    SAE is a technical/engineering organization – not advocacy/policy/law
    Target audience: Vehicle manufacturers – not infrastructure etc.
    Issues unique to ADS-DVs - not wheelchair securements, lifts, etc. as these are covered by J1725, J2092, J2093, & J2249
Focused on road worthy vehicles in a fleet-based shared mobility
Information report on issues to be considered – not a standard
J3171 Draft
<number>
Notes: SAE J1725 Structural Modification for Personally Licensed Vehicles to Meet the Transportation Needs of Persons with Disabilities
SAE J2092 Testing of Wheelchair Lifts for Entry to or Exit from a Personally Licensed Vehicle
SAE J2093 Design Considerations for Wheelchair Lifts for Entry to or Exit from a Personally Licensed Vehicle
SAE J2249 Wheelchair Tiedown and Occupant Restraint Systems for Use in Motor Vehicles
<number>

## Slide 3: Method
Review of Driver’s License Requirements
    Each state requires that individuals pass a knowledge test, a vision test, & a skills test to obtain a driver’s license.
    Meeting these requirements is unlikely for individuals with certain cognitive, and/or vision disabilities. This was the initial focus – but further research broadened scope.
Literature Review
    Work currently being done to involve PWDs in design of technology of any kind
    International best practices in accessible transportation
Stakeholder Interviews
J3171 Draft
<number>
PWD = person with disability
PWDs | identify barriers & workarounds
Advocates & others who work with PWDs | identify barriers & workarounds
Experts in design for PWDs | Identify existing knowledge in universal design that could be applied to design of ADS-DVs
Government/policy experts knowledgeable about transportation and/or PWD | Identify policy measures that may facilitate ADS-DV passenger accessibility as it relates to certain PWDs

## Slide 4: Organization of Design Guidance/Issues
J3171 Draft
<number>
Difficulty of Classifying Disabilities
General Design Guidance
Specific Guidance for ADS-DVs

## Slide 5: Difficulty Classifying People With Disabilities
jJ3171 Draft
<number>
Traditional Classification: Portion of body impacted & severity of that impact
    However doesn’t address individual differences
    Assumes disability is a deficiency
WHO’s International Classification of Functioning, Disability & Health:
    disability is only a problem when the individual tries to function in a world that has barriers
    great deal of individual differences with regard to what is a barrier within a traditionally classified disability
    classification of the disabilities can only be done in relation to an activity and its barriers
    removing barriers – removes disability

## Slide 6: Organization of Design Guidance/Issues
J3171 Draft
<number>
Difficulty of Classifying Disabilities
General Design Guidance
    Considering Barriers in Design
    Universal Design Principles
    Goals of Universal Design
    Accessible HMI Standards
Specific ADS-DV Issues
Notes: <number>

## Slide 7: Considering Barriers in Design
J3171 Draft
<number>
Although ADS-DV may remove barrier of Driver’s license – design of vehicles could add in new barriers
Generally makes things more user friendly to all
    E.g., curb cutouts great for people with strollers/ luggage
Technology that is highly user-friendly to PWDs have accessibility settings that allow persons to customize their experience

## Slide 8: Universal Design Principles
J3171 Draft
<number>
Equitable use | Great user experience/safety for everyone
Flexibility in use | Tasks can be performed by those with differing abilities
Simple & intuitive use | Don't make me think; KISS
Perceptible information | Multimodal; Considers impact of environment (sun, noise)
Tolerance for error | Prevents mistakes; Makes error recovery easy
Low physical effort | Operable without contortion or exertion; by either hand
Size & shape for approach & use | Usable by different body shapes, sizes, & productivity tools
Connell et al (1997) paid for by National Institute for Disability & Rehabilitation research under the U.S. Department of Education

## Slide 9: Goals of Universal Design
Body fit: accommodating a wide range of body sizes and abilities. This means ensuring the participants in tests include the 5th percentile female to the 95th percentile male as well as people who have various physical disabilities that could affect how they interact with an ADS-DV.
Comfort: keeping demands within desirable limits of body function and perception. This means ensuring the participants in tests include people with various sensory and physical disabilities to evaluate if they can interact successfully with the ADS-DV.
Awareness: ensuring that critical information for use is easily perceived. This means including people with various sensory disabilities as participants in product tests to ensure that they can perceive all critical information.
Understanding: making methods of operation and use intuitive, clear and unambiguous. This means ensuring the participants in tests include people with mild cognitive impairments to evaluate if the system is easy to use.
Personalization: incorporating opportunities for choice and the expression of individual preferences (i.e., customization of experience)
Wellness, Social Integration, & Cultural Appropriateness were not included as they were outside of the scope of the document
J3171 Draft
<number>
Steinfeld & Maisel (2012) presented 8 goals: 4 of which are discussed in SAE report as helpful for testing & 1 for designers
Testing
Testing
Design

## Slide 10: Accessible HMI Standards
Section 508 of the Rehabilitation Act of 1973
Web Content Accessibility Guidelines (WCAG) – by the World Wide Web Consortium (W3C)
J3171 Draft
<number>

## Slide 11: Organization of Design Guidance/Issues
J3171 Draft
<number>
Difficulty of Classifying Disabilities
General Design Guidance
Specific Issues for ADS-DVs
    Individuals with Visual Impairments
    Wheeled Mobility Device users
    Individuals with Other Disabilities

## Slide 12: Issues for those with Visual Impairments
On & Off-Boarding
    Wayfinding
    Identification of ADS-DV
    Barrier free path
In-Vehicle Communications
    Confidence going to right location in most efficient way
    Emergency scenarios – e.g., support decision to stay within or exit vehicle
J3171 Draft
<number>
Notes: Wayfinding -- spatial problem solving. It is knowing where you are in a building or an environment, knowing where your desired location is, and knowing how to get there from your present location.
<number>

## Slide 13: Wheeled Mobility Device (WMD) Users: Accessible On & Off Boarding Location
Generally
    Not always main entrance
    Travelling downhill easier than uphill
For Those Who Can Transfer Themselves to Vehicle Seat
    3ft wide space parallel to vehicle without barrier (e.g., curb, other vehicle)
    Seat height supports transfer
    Flat location
For Those Who Remain within WMD
    Size & location (rear or side) of ramp/chair lift is considered
    Space to maneuver WMD to enter ramp/lift is provided
    Direction of approach to vehicle/destination is considered
J3171 Draft
<number>
Notes: <number>

## Slide 14: Issues for those with Other Disabilities
Other Mobility Disabilities
    Short distance to accessible entrance of origin/destination
    Negotiating curbs is challenging for some
Other Sensory Disabilities
    All in-vehicle communication particularly for emergencies should be perceptible by all (i.e., hearing impairments; “deaf & blind”)
    Not overwhelming to those with sensory processing disorders (i.e., autism spectrum)
J3171 Draft
<number>
Notes: <number>